## Slide 1: Triangular mesh generation from 2D CT image
Arjun Kumar, Bo Ning, Xiaodong Wei

## Slide 2: Outline
Problem Definition
  Application: Fuel cells
  Input: CT Image
  Output: Triangular mesh of 2D slice
    Uniform and adaptive
Pre-processing
  Quadtree subdivision
Algorithm
  Marching Squares
Implementation
Results

## Slide 3: Our Specific Application
Fuel cells - Diffusion media, anode and cathode are porous materials, whose geometry can be important to the performance of the cell
Their geometry is captured using nanoscale X-ray CT imaging
Meshes are required to run simulations using that geometry
  Possible applications also for 3D printing
Schematic of diffusion media, anode and catalyst in fuel cell
Streamlines showing results of a diffusion simulation in diffusion media

## Slide 4: Input Image
We take a slice of a 3D image of cathode of fuel cell
We test our method with simple images for the slice of the 3D image
One of the things we hope to achieve is to mesh both solid and air phases that are conformal to the boundary to simulate interphase transport
Segmented 3D image of cathode and slice selection
Input 2D image for project (blue = solid)

## Slide 5: Images for Testing

## Slide 6: Pre-processing: Quad-Tree Subdivision
For adaptive mesh generation, quadtree subdivision will allow us to use less triangles far away from the boundary and more more near the boundary
Hanging Node - limit to one for convenience and quality of triangles
Multiple One
Hanging Hanging
Nodes: Node:
Poor OK

## Slide 7: Subdivision Implementation
Breadth first search tree traversal
Have to traverse backwards to keep depth of tree balanced

## Slide 8: Transformation: Method
Marching squares
One of the most widely used methods in mesh generation from image data
Marching squares visits each cell of input image, and generate one or more polygons for each cell that represents the material
  Cell: each vertex has a value (0 or 1) to indicate material or air
  Material (1): black dots
  Air (0): circles

## Slide 9: Transformation: Method
Marching squares
Configuration of cells
  16 cases depending on how vertices can be colored
  Can be mapped to 6 cases

## Slide 10: Transformation: Method
Marching squares
Triangulation of cells
  Generate middle points of color-changed edges (green dots)
  Add edges to obtain triangles (blue)

## Slide 11: Transformation: Method
Marching squares
Connection with quad-tree subdivision
  Cells with hanging node on edges (blue dots)
  Restrict at most one hanging node on one edge
  5 cases depending on the position and number of handing nodes

## Slide 12: Transformation: Method
Marching squares
Uniform mesh generation
  Without quad-tree subdivision
  Done
Adaptive mesh generation
  With quad-tree subdivision

## Slide 13: Post-processing: STL and VRML File Generation
STL file
File with simple syntax to represent the generated mesh
No many feature for color, polynomial and other information
Not very effective to demonstrate our workflow
VRML file
File with many features to represent the geometric information
Large files for very complex geometry
Our major way to work on
Triangular Mesh
Rectangular Quad-Tree
Base Image

## Slide 14: Object Model
Initial Design
ImageMeshConvertor
GDLImage
Mesh
Issues
No way to perform varied methods in concrete implementation
Objects are intervening with each other
Not good for task distribution for three members

## Slide 15: Object Model
Final Design
Application Class
Controller to store the shared data, invoke the major routines
ImagePreLie Class
Preprocessing class to read images and generate quad-trees
Image2TriMesh_2D Class
Transformation class to do image to mesh transformation
PostProcessor Class
Post-processing class to collect the data and generate files
Preprocessor
(Arjun)
Transformer
(Xiaodong)
Postprocessor
(Bo)
Controller

## Slide 16: Implementation
Object Oriented Programming with C++
We are implementing the program with C++ in Linux Platform
Cmake to build the project
Build automation
Version Control & Collaboration
We are using Github to work on the project collaboratively, the URL of our project repository is in: https://github.com/bning/CADCourseProject
Open Source Resources
glm library for some geometric calculation
Cortona3D to render the images, quad-trees and meshes

## Slide 17: Results
Uniform Mesh Generation
TestCircle
TestDoubleTorus

## Slide 18: Results
Issues
Not representative for the details and fine regions
Low efficiency in transformation and post-processing
Would give very large files that are slow to load and render
GDLImage

## Slide 19: Results
Quadtree for adaptive mesh generation
TestCircle
TestDoubleTorus

## Slide 20: Results
Quadtree for
adaptive mesh generation
GDLImage

## Slide 21: Thanks
Questions?